Vorläufige Materialliste - Sara Nemtsov – NUN – 21.10.2019

1. General description of the electronic part

The electronics of Sarah Nemtsov’s “NUN” consist of two main parts
Each instrument is processed by two effects with each different presets that are changed during the piece. The effects are (de-)activated by the musicians on stage. The three string players and the three wind players have a switch pedal and an expression pedal each. The switch pedal enables or disables the effects on the corresponding instrument. The expression pedal controls the general volume after the effects processing.
Furthemore four instrument groups (strings, percussion, piano and winds) are routed to a speaker positionend behind or above the musicians and an exciter attached to a percussion instrument set in front.
The electronics 1 performer has a laptop on stage and performs many different tasks. On one side, it has an expression pedal to control the volume of the piano. He/She also controls the different parameters of the effect affecting the piano., he/she is responsible of switching all the instrument between the speakers and audio exciters attached to the percussion instruments on front. And last but not least this performer plays back seven audio files over the stereo PA in front of the stage.
The electronics 2 performer has a Wii controller that affects the different effect’s parameters applied to the percussion. This part can also be performed by the conductor.

2. Audio setup

All instruments are to be miced very close, ideally with clip microphones. The microphones are first plugged into the mixing console and each signal outputed as direct out into the audio interface, with the exception of percussion and piano, who first need to be summed into a bus and then outputed, because the patch takes only one input per instrument. The computer on stage doesn’t have to be sent into the patch.
The patch returns 16 channels of audio two for each instrument: one for the speaker and one for the exciter. The sound director then needs to route this signals to the corresponding output.

3. MIDI Setup

The computer on stage also acts as a midi central station. All switch as well as expression pedals need to be plugged to this computer. For that you will need a switch to midi converter, a pedal to midi converter and an external MIDI interface with at least 8 Inputs and one output.
The MIDI channels and Control values are to be set up as following:

Control Number	Channel	Parameter in Patch	Device
1	1	Violine FX On/Off	Switch Pedal Violine
1	2	Viola FX On/Off	Switch Pedal Viola
1	3	Cello FX On/Off	Switch Pedal Cello
1	4	Percussion FX On/Off	Switch Pedal Drums
1	5	Piano FX On/Off	Switch Pedal Piano
1	6	Sax FX On/Off	Switch Pedal Sax
1	7	Oboe FX On/Off	Switch Pedal Oboe
1	8	Clarinet FX On/Off	Switch Pedal Clarinet
7	1	Volume Violine	Volume Pedal Violine
7	2	Volume Viola	Volume Pedal Viola
7	3	Volume Cello	Volume Pedal Cello
7	4	Volume Percussion	Volume Pedal Drums
7	5	Volume Piano	Volume Pedal Piano
7	6	Volume Sax	Volume Pedal Sax
7	7	Volume Oboe	Volume Pedal Oboe
7	8	Volume Clarinet	Volume Pedal Clarinet
3	1	strings output routing	MIDI Controller
3	2	percussion output routing	MIDI Controller
3	3	piano output routing	MIDI Controller
3	4	winds output routing	MIDI Controller

4. The Patches

4.1 NUN_STAGE.pd (Stage Patch)
MIDI

7x Expression Pedale – link
+ TRS Klinkenkabel
7x Pedal to MIDI converter – link
+ 7x MIDI Kabel
6x Switch Pedale – link
+ 6x Kopfhörerverlängerung
6x Footswitch to MIDI (oder 1x 8-Fach) – link
MIDI → USB Interface mit mindestens 8 Intpus und 2 Outputs – link
MIDI Controller (optional aber empfohlen!)

WII Controller + Nunchuk - link
Bluetooth 4.0 USB Dongle - link
USB Verlängerung

RECHNER
1x Laptop (Bühne) mit PureData und Oscullator (+1x als Backup) + Audiointerface (2x Output)
Den Rechner muss 2x USB Ports ) + 1x Netzwerk Port (RJ45) haben.
1x Laptop (FOH) mit Puredata (+1x als Backup) + Audiointerface (8x Input, 10x Output, Dante Virtual Sound Card sehr empfohlen).
Den Rechner muss 1x USB Port und 1x Netzwerk Port (RJ45) haben.

NETZWERK
2x switch (8 busse) - link
2 RJ45 cat5 Kabeltrommel (Bühne bis FOH, ca 50m) → Im WDR eventuell nicht nötig
10 RJ45 Patchkabel

AUDIO
4x full range Lautsprecher (Bühne)
2x full range Lautsprecher (PA)
4x Exciter + Verstärker (Sarah hat welche gekauft, vielleicht kann sie sie selber mitbringen) - link
8x dpa4099 (Vl, Va, Vo, 2x Pno, Sax, Kl, Ob Klemmen) (Mikrofone für Schlagwerk fehlen!!)
Audio Interface (8x Input, 16x Output)

SOFTWARE

PureData 0.50 (open-source und kostenlos)
Osculator – link