Sarah Nemtsov – NUN

Abstractions
[arctan_distortion] : Overdrive effect using the arctan function
Arguments: Gain, Volumen, Receive symbol

[wahwah] :
Arguments: modulator frequency, depth, center frequency, filter Q, dry/wet ratio, receive symbol

[tremolo] : amplitude modulation
Arguments: modulation frequency, depth, receive symbol

[ring]: ring modulator
Arguments: modulation frequency, depth, receive symbol

[pitch_shifter] : Pitch shifter (delay based)
Arguments: transposition, modulation frequency, receive symbol

[gs~] : granular sampler
Arguments: signal (100 a 4000), sample (30 a 60), feedback (on/off), receive symbol

[harmonizer] : Harmonizer based on the pitch shifter abstraction
Arguments: shift (semitornes) voice1, voice 2, voice 3, voice 4
An argument of 0 sends the original signal thru.

[chorus] : based on a delay line with modulated reading heads
Arguments: modulation frequency {v1, v2, v3, v4, all}(in Hz), modulation amplitude {v1, v2, v3, v4, all}, receive symbol

[mod_hpf] : Modulated high pass filter
Arguments: modulation frequency (Hz), modulation amplitude, centre frequency, receive symbol

[flanger] : flanger effect
Arguments: modulation frequency (Hz), modulation amplitude, feedback (max 0.95), receive symbol

[delayFX] = simple delay with feedback
Arguments: delay time (ms), feedback (%), receive symbol

MIDI

Control Number	Channel	Parameter in Patch
1	1	Violine FX On/Off
1	2	Viola FX On/Off
1	3	Cello FX On/Off
1	4	Percussion FX On/Off
1	5	Piano FX On/Off
1	6	Sax FX On/Off
1	7	Oboe FX On/Off
1	8	Clarinet FX On/Off
7	1	Volume Violine
7	2	Volume Viola
7	3	Volume Cello
7	4	Volume Percussion
7	5	Volume Piano
7	6	Volume Sax
7	7	Volume Oboe
7	8	Volume Clarinet
3	1	strings output routing
3	2	percussion output routing
3	3	piano output routing
3	4	winds output routing

OSC

fx_pedal/[instrument]/[0,1] // switches between clean and fx
express/[instrument]/[0,127] // expression pedal
output_routing/[instrument group]/[speaker, transducer]/[0,1] // switches between speaker	and transducer

From Osculator to pd
wii/accel/pitch/[0-1] // movement front to backward
wii/accel/roll/[0-1] // movement to the sides
wii/accel/yaw/[0-1] //
wii/button/one/[0-1] // momentary button one
wii/button/two/[0-1] // momentary button two
wii/button/A/[0-1] // momentary button A

instruments = [violine, viola, cello, percussion, piano, sax, oboe, clarinet]
instrument group = [strings, percussion, piano, winds]