Vorläufige Materialliste - Sara Nemtsov – NUN – 21.10.2019

General description of the electronic part

The electronics of Sarah Nemtsov’s “NUN” consist of two main parts
Each instrument is processed by two effects with each different presets that are changed during the piece. The effects are (de-)activated by the musicians on stage. The three string players and the three wind players have a switch pedal and an expression pedal each. The switch pedal enables or disables the effects on the corresponding instrument. The expression pedal controls the general volume after the effects processing.
Furthemore four instrument groups (strings, percussion, piano and winds) are routed to a speaker positionend behind or above the musicians and an exciter attached to a percussion instrument set in front.
The electronics 1 performer has a laptop on stage and performs many different tasks. On one side, it has an expression pedal to control the volume of the piano. He/She also controls the different parameters of the effect affecting the piano., he/she is responsible of switching all the instrument between the speakers and audio exciters attached to the percussion instruments on front. And last but not least this performer plays back seven audio files over the stereo PA in front of the stage.
The electronics 2 performer has a Wii controller that affects the different effect’s parameters applied to the percussion. This part can also be performed by the conductor.

Equipment

In order to perform the piece you will need the following equipment:

MIDI

7x Expression Pedals
7x Pedal to MIDI converter (I recommend the “Pedal to MIDI Converter” from MIDI Solutions)
6x Switch Pedals (Like the sustain pedal used for Keyboards)
6x long 6.3mm extension Jack cables (one side male and the other female)
6x Footswitch to MIDI (or one where you can plug 6, I recommend the F8 Footswitch / MIDI Converter from MIDI Solutions)
MIDI → USB Interface with at least 8 Intputs und 2 Outputs (and if possible a couple of USB Inputs, I recommend the ESI M8U eX)
MIDI Controller, with 4 buttons and 4 faders or dials (optional but recommended)

WII Controller + Nunchuk
Bluetooth 4.0 USB Dongle
USB extension cable

Computer

1x MacBookPro (Stage) with PureData und Oscullator + Audio interface (2x Output)
This computer must have at least 2x USB ports and 1x network port (RJ45).
1x Laptop (FOH) with Puredata + Audiointerface with at least 8x Input and 16x Output.
This computer must have at least 1x USB port and 1x network port (RJ45).

I strongly recommend to use a backup for at least the computer at the front of house, ideally for both.

Network
2x gigabit switches
2x long RJ45 cat5 cables (stage to foh)
10x RJ45 patch cables

Audio
4x full range loudspeakers on stage (on stands or hanging behind/above the musicians)
2x full range loudspeakers in front of the stage (like normal PA position)
4x audio exciter + amplifiers (I used the DAEX32EP-4 Thruster 32mm Exciter 40W 4 Ohm from Dayton Audio)
8x clip microphones with clips for Violin, Viola, Cello, 2x Piano, Sax, Clarinet, Oboe (I recommend dpa4099) (Mikrofone für Schlagwerk fehlen!!)
2x audio interface (one with 2x outputs and the other with at least 8x inputs, 16x outputs)

Software

PureData 0.50 or later - http://msp.ucsd.edu/software.html
Osculator 3.0 – https://osculator.net/

Audio setup

All instruments are to be miced very close, ideally with clip microphones. The microphones are first plugged into the mixing console and each signal outputed as direct out into the audio interface, with the exception of percussion and piano, who first need to be summed into a bus and then outputed, because the patch takes only one input per instrument. The computer on stage doesn’t have to be sent into the patch.
The patch returns 16 channels of audio two for each instrument: one for the speaker and one for the exciter. The sound director then needs to route this signals to the corresponding output.

MIDI Setup

The computer on stage also acts as a midi central station. All switch as well as expression pedals need to be plugged to this computer. For that you will need a switch to midi converter, a pedal to midi converter and an external MIDI interface with at least 8 Inputs and one output. It is better if the MIDI converters are configurable; if not you will need to change the CC values in the patch.

The Patches

There are two patches that belong to the piece.
It is very important that you don’t change the folder structure, or move the patches somewhere else. If you need a fast access to the patches make a shortcut or alias but don’t move them.

NUN_STAGE.pd (Stage Patch)

This is the patch that the electronics performer 1 plays with the computer on stage. With the help of a MIDI controller or the computer keyboard the performer can route the different instrument groups to the speakers or the exciter, play the seven audio files for the PA and manipulate the parameters of the piano effects.
In the background, this patch also functions as a translator between MIDI and osc, and also sends all the translated information to the FOH patch. This is done in the background, the interface is hidden to the performer.

Setup

Before opening the patch (or PD) check that you have all the peripherals plugged to the computer. Then open the patch by double click or if you already have opened PureData, file → Open and search for the file with the file manager.
Then you need to configure the MIDI and Audio settings. For MIDI you click media → MIDI Settings… and you should see something like this:

By clicking on the device’s name you get a drop down menu where you can choose which devices you want to get MIDI from (Input) and to which devices you want to send MIDI to (output). You need to set your MIDI interface and controller as input and your interface only as output. Make sure to put your MIDI interface in the first slot. PureData interprets the MIDI channel of the controller in the 2nd slot as being 16 channels higher than the controller really is (so if your controller sends to channel one, PureData will interpret it to be sending on channel 17). Each higher slot adds than 16 channels to the controller.

The Audio setup dialog is very similar. You go to media → Audio Settings… and select your external sound card as input and output. Here you also need to make sure that the sampling rate is set to 48000. If you click the “save all settings” button, the configuration will be saved even if you close the program.

Usage

After you open the patch you should see something like this:

By pressing INIT you initialize the patch and are ready to start the piece.

4.2 NUN_FOH.pd (FOH Patch)

This patch does all the audio processing for the piece. I takes one input per instrument (see the list below) and outputs two channels for each instrument, the first to be routed to the corresponding speaker behind the performers and the other one to the exciters.

Setup

The audio and MIDI setups are the same as with the stage patch, but of course you need to select the right interface plugged to your computer.

Usage
Explanation of how to use the patch.

4.2.1 Patch IO

Patch Input	Expects Signal...
1	Violine
2	Viola
3	Cello
4	Percussion
5	Piano
6	Sax
7	Clarinet
8	Oboe

Patch output	Outputs Signal...
1	Violin Speaker
2	Violin Exciter
3	Viola Speaker
4	Viola Exciter
5	Cello Speaker
6	Cello Exciter
7	Percussion Speaker
8	Percussion Exciter
9	Piano Speaker
10	Piano Exciter
11	Sax Speaker
12	Sax Exciter
13	Clarinet Speaker
14	Clarinet Exciter
15	Oboe Speaker
16	Oboe Exciter

The MIDI channels and Control values are to be set up as following:

Control Number	Channel	Parameter in Patch	Device
1	1	Violine FX On/Off	Switch Pedal Violine
1	2	Viola FX On/Off	Switch Pedal Viola
1	3	Cello FX On/Off	Switch Pedal Cello
1	4	Percussion FX On/Off	Switch Pedal Drums
1	5	Piano FX On/Off	Switch Pedal Piano
1	6	Sax FX On/Off	Switch Pedal Sax
1	7	Oboe FX On/Off	Switch Pedal Oboe
1	8	Clarinet FX On/Off	Switch Pedal Clarinet
7	1	Volume Violine	Volume Pedal Violine
7	2	Volume Viola	Volume Pedal Viola
7	3	Volume Cello	Volume Pedal Cello
7	4	Volume Percussion	Volume Pedal Drums
7	5	Volume Piano	Volume Pedal Piano
7	6	Volume Sax	Volume Pedal Sax
7	7	Volume Oboe	Volume Pedal Oboe
7	8	Volume Clarinet	Volume Pedal Clarinet
3	1	strings output routing	MIDI Controller
3	2	percussion output routing	MIDI Controller
3	3	piano output routing	MIDI Controller
3	4	winds output routing	MIDI Controller