Index

- General description of the electronic part
- Description of the audio part
- List of equipment
- The patches
- Setting up
- Notes for the electronics director
- Notes for the sound director
- Notes for the electronics assistant
- Apendix osc routes, midi notes, etc

## General description of the electronic part

The electronics of Sarah Nemtsov’s “NUN” consist of two main parts
Each instrument is processed by one or more effects, some with different presets that are changed during the piece. The effects are (de-)activated by the musicians on stage by pressing a pedal. The switch pedal enables or disables the effects on the corresponding instrument.
Furthemore the four instrument groups (strings, percussion, piano and winds) are switched to the speaker positioned behind or above the musicians or to an exciter attached to a percussion instrument set in the front.
There is an optional wii controller that can be worn by the conductor that modulates some of the instruments’ effects.
I very much recommend to have two humans on the FoH, one doing only the electronics and another one doing the sound direction

## Description of the audio part

Nun is a powerful piece with a very direct (or near) sound. Nevertheless is important to create some localisation for the instruments on stage. It is important to have one speaker for each instrument, directly behind of the player. Depending on the room characteristics it may be necessary to also send some of the instruments to the main PA, but the localisation should remain on the performer’s position on stage.
I strongly recommend the use of clip microphones on all the instruments, including the piano and the drum set toms. Because of the effects, some of the playbacks and the general sound of the piece there are some similarities to pop music, those are desired and part of the piece.
The main PA system needs to be powerful enough with good coverage in the bass frequencies.
Some stretches of the piece sound very overwhelming and chaotic, enjoy them!
The conductor muss have a monitor to hear the electronics. Depending on the stage setup, the pianist and drum set player might also need monitors to hear each other because they play a lot together.

## Equipment

In order to perform the piece you will need the following equipment:

### MIDI

6x Switch Pedals (Like the sustain pedal used for Keyboards)
6x long 6.3mm extension Jack cables (one side male and the other female)
6x Footswitch to MIDI (or one where you can plug 6, I recommend the F8 Footswitch / MIDI Converter from MIDI Solutions)
MIDI → USB Interface with at least 8 Intputs und 2 Outputs (and if possible a couple of USB Inputs, I recommend the ESI M8U eX)
MIDI Controller, with 20 buttons (optional but recommended)

Optional
WII Controller + Nunchuk
Bluetooth 4.0 USB Dongle
USB extension cable

### Computer

1x MacBookPro (Stage) with PureData und (optional) Oscullator.
This computer must have at least 2x USB ports and 1x network port (RJ45).
1x Laptop (FOH) with Puredata + Audiointerface with at least 8x Input and 16x Output. At the time of writing is possible to use the Dante Virtual Soundcard.
This computer must have at least 1x USB port and 1x network port (RJ45).

I strongly recommend to use a backup for at least the computer at the front of house, ideally for both.

### Network

1x gigabit switches
1x long RJ45 cat5 cables (stage to foh)
10x RJ45 patch cables

### Audio

8x full range loudspeakers on stage (on stands or hanging behind/above the musicians)
2x full range loudspeakers in front of the stage (like normal PA position) + subwoofers
4x audio exciter + amplifiers (I used the DAEX32EP-4 Thruster 32mm Exciter 40W 4 Ohm from Dayton Audio)
12x clip microphones with clips for Violin, Viola, Cello, 2x Piano, Sax, Clarinet, Oboe, Drums [Snare and 3x Toms] (I recommend dpa4099) + 1x Microphone for the Bass Drum, and two Overheads for the cymbals
4x small membrane condenser microphones, for the instruments that are excited by the transducers
1x audio interface (one with 2x outputs and the other with at least 8x inputs, 16x outputs) (already listed on the computer part)
Mixing desk with at least 36 inputs and 24 outputs

### Software

PureData 0.50 or later - http://msp.ucsd.edu/software.html
Osculator 3.0 – https://osculator.net/ (optional, only needed if the wii controller is used)

# Setting up
## Audio setup

All instruments are to be miced very close, ideally with clip microphones. The microphones are first plugged into the mixing console and each signal outputed as direct out into the audio interface, with the exception of percussion and piano, who first need to be summed into a bus and then outputed, because the patch takes only one input per instrument. For the drum bus some testing and experimentation with the individual signal levels might be needed, to best find a balance that works for all the effects. I recommend to start sending the toms and snare only, and then maybe add some of the bass drum. The overheads tend to have too much leakage from all the other instruments (and speakers) on stage, so they will be probably not needed on the FX bus that goes into the computer.
The patch returns 14 channels of audio in total. One for each processed instrument, four for the exciters and two for the soundtracks that go to the main PA. The sound director then needs to route this signals to the corresponding output.
A note regarding the exciter’s output: after performing the patch with another setup I decided to add all the outputs that go to each transducer inside the patch. This means that for example if the strings are routed to the transducer the patch outputs a sum of all three strings. So it is not possible to change the balance between the strings that go into the exciter. This doesn’t really matter, as when the instruments are sent to the exciters the resulting sound is more like an effect than anything. It is not possible to distinguish between the single instruments in this case, so a very precise balance control is not needed. This reduces the amount of needed outputs by 8, which I found to be a big benefit for a piece that already needs a lot signal exchange between the mixer and the computer.

## MIDI Setup

The computer on stage also acts as a midi central station. All switch pedals need to be plugged to this computer. For that you will need a switch to midi converter and an external MIDI interface with preferably four Inputs and four outputs. It is better if the MIDI converters are configurable; if not you will need to change the CC values in the patch. A detailed documentation about the MIDI CC notes and channels used can be found in Apendix
A note on the Midi Solutions products (at least the ones I had to use): all the pedal/switch to midi converters are powered via the input/thru midi port on the device. The company sells some adapters for midi/dc power supply, but this is actually not needed. All you need to do is plug some device to the midi converter’s input and send them a midi note or command. On the stage patch sends a midi cc and note on startup to initialize the converters.

## Network setup

This part is actually quite straight forward, it is important only important to open the FOH patch first, because if the stage patch is opened first and tries to open the connection will fail. Then you only need to check that the stage patch has the correct ip address configured on the object and everything should work. You can turn on the autockeck on the stage patch to send all parameters automatically to see if you have a connection. You can also click the [print network messages] box to see the incoming messages on the console.
# Notes for the electronics director

it is important to know the piece very well and being able to “interfere” and correct some mistake that the performers may make.
Each instrument (group) has two different “effect states”, wet and dry, and to “output routing states”, speaker and transducer. In order to have some independence between the amplification and the electronics, the patch behaves differently depending on the combination. The following table illustrates the concept using the violin as an example, but it is the same for all instruments.
Signal	FX	Routing	Result
violine	on	speaker	comes out of the output 1 and should be routed to the speaker
violine	off (bypassed)	speaker	nothing comes out of the patch (should only be directly amplified)
violine	on	transducer	comes out of output 11 and goes to the donnerblech
violine	of (bypassed)	transducer	comes out of output 11 and goes to the donnerblech

This can be somewhat confusing but without this behaivior the slightly delayed dry signal going to the speakers would mix with the already present dry amplification and cause comb filtering.
# The Patches

There are two patches that belong to the piece.
It is very important that you don’t change the folder structure, or move the patches somewhere else. If you need a fast access to the patches make a shortcut or alias but don’t move them.

NUN_STAGE.pd (Stage Patch)

This is the patch that the electronics performer 1 plays with the computer on stage. With the help of a MIDI controller or the computer keyboard the performer can route the different instrument groups to the speakers or the exciter, play the seven audio files for the PA and manipulate the parameters of the piano effects.
In the background, this patch also functions as a translator between MIDI and osc, and also sends all the translated information to the FOH patch. This is done in the background, the interface is hidden to the performer.

Setup

Before opening the patch (or PD) check that you have all the peripherals plugged to the computer. Then open the patch by double click or if you already have opened PureData, file → Open and search for the file with the file manager.
Then you need to configure the MIDI and Audio settings. For MIDI you click media → MIDI Settings… and you should see something like this:

By clicking on the device’s name you get a drop down menu where you can choose which devices you want to get MIDI from (Input) and to which devices you want to send MIDI to (output). You need to set your MIDI interface and controller as input and your interface only as output. Make sure to put your MIDI interface in the first slot. PureData interprets the MIDI channel of the controller in the 2nd slot as being 16 channels higher than the controller really is (so if your controller sends to channel one, PureData will interpret it to be sending on channel 17). Each higher slot adds than 16 channels to the controller.

The Audio setup dialog is very similar. You go to media → Audio Settings… and select your external sound card as input and output. Here you also need to make sure that the sampling rate is set to 48000. If you click the “save all settings” button, the configuration will be saved even if you close the program.

Usage

After you open the patch you should see something like this:

By pressing INIT you initialize the patch and are ready to start the piece.

4.2 NUN_FOH.pd (FOH Patch)

This patch does all the audio processing for the piece. I takes one input per instrument (see the list below) and outputs two channels for each instrument, the first to be routed to the corresponding speaker behind the performers and the other one to the exciters.

Setup

The audio and MIDI setups are the same as with the stage patch, but of course you need to select the right interface plugged to your computer.

Usage
Explanation of how to use the patch.

4.2.1 Patch IO

Patch Input	Expects Signal...
1	Violine
2	Viola
3	Cello
4	Percussion
5	Piano
6	Sax
7	Clarinet
8	Oboe

Patch output	Outputs Signal...
1	Violin Speaker
2	Violin Exciter
3	Viola Speaker
4	Viola Exciter
5	Cello Speaker
6	Cello Exciter
7	Percussion Speaker
8	Percussion Exciter
9	Piano Speaker
10	Piano Exciter
11	Sax Speaker
12	Sax Exciter
13	Clarinet Speaker
14	Clarinet Exciter
15	Oboe Speaker
16	Oboe Exciter

The MIDI channels and Control values are to be set up as following:

Control Number	Channel	Parameter in Patch	Device
1	1	Violine FX On/Off	Switch Pedal Violine
1	2	Viola FX On/Off	Switch Pedal Viola
1	3	Cello FX On/Off	Switch Pedal Cello
1	4	Percussion FX On/Off	Switch Pedal Drums
1	5	Piano FX On/Off	Switch Pedal Piano
1	6	Sax FX On/Off	Switch Pedal Sax
1	7	Oboe FX On/Off	Switch Pedal Oboe
1	8	Clarinet FX On/Off	Switch Pedal Clarinet
7	1	Volume Violine	Volume Pedal Violine
7	2	Volume Viola	Volume Pedal Viola
7	3	Volume Cello	Volume Pedal Cello
7	4	Volume Percussion	Volume Pedal Drums
7	5	Volume Piano	Volume Pedal Piano
7	6	Volume Sax	Volume Pedal Sax
7	7	Volume Oboe	Volume Pedal Oboe
7	8	Volume Clarinet	Volume Pedal Clarinet
3	1	strings output routing	MIDI Controller
3	2	percussion output routing	MIDI Controller
3	3	piano output routing	MIDI Controller
3	4	winds output routing	MIDI Controller